INSTRUCTIONS FOR GLASSWASHER USE

Detergent   Check Detergent Containers for auto dosing systems

Operation

- Push Power / Start switch  to turn machine on ( door Closed )  automatically fills -

NOTE: The machine will take several minutes to reach operating temperatures

- Wait till Temp - ( 3 ) -  wash reads 60 deg C  and ( 5 ) Rinse reads 82 deg C ( Digital Display)

- Scrape down heavily soiled plates into a waste bin, rinse off all food

Do not put heavily soiled plates into the machine

waste product may block the machine when draining pre-rinse all items

- Insert rack with plates, glassware, cups,  cutlery etc to be washed

- Press cycle select switch  ( select 1 for 60 sec and 2 for 120 sec wash ) to start cycle

- After wash and rinse cycle  - light stops flashing  -  remove rack

The machine is now ready for another load

Cleaning

Each day empty and clean the wash tank . remove Drain Plug

With Door closed – select Drain   and press start button    - Light flashing

Machine now drains and cleaning cycle begins - at end of cleaning cycle turn machine off

Call  1300 217 411 for all detergent and service requirements

# Text boxes

PH 1300 217 411

www.warewashingsolutions.com.au

Rinse Temp

Wash temp

Start Cycle

Cycle Select

Power on/off

# Remove bottom filter ,

# Wash and rinse then replace in position

# check wash arms are not   blocked  and  moving freely

# Clean inside of machine

# Leave door open for ventilation   END OF DAY ---Turn Machine Off